Basic Layout of Huawei OLT

Basic Layout

Chassis: bundled sales, not sold separately

MPU: generally double master, one for main and one for standby, SCUN, MCUD (MA5608T) are common used

Power Plate: generally dual power, one for main and one for standby, PRTE (DC), MPWC (DC), MPWD (AC) are common used

Upstream board: GICF, GICG, X2CS etc.

GPON service boards: GPBD, GPFD etc.

Software: generally has been installed inside the control board SCUN

Control board - SCUN (SCUL, SCUK, SCUH)

Function:

- Systematic control, switching and unified network management

- Simple routing protocol functions realization

External Interface:

- CON (RS-232 the serial port maintenance)

- ETH (10/100M Base-T the Ethernet port maintenance)

- ESC environmental monitoring port

- 4 GE uplink optical interfaces

Frequently configure two, one for main and one for standby, OLT software is installed in the main control board

GPON service board -GPBC/GPBD/GPFD

Main functions:

Huawei GPON (Gigabit Passive Optical Network) access panel and terminal ONU (Optical Network Unit) devices together to achieve the OLT function on GPON system, default with B + SFP module (free), to replace the need to purchase C +

Differences of GPON board:

| Type | Port number | Optical module | Maximum splitting ratio | Traffic shaping |
| --- | --- | --- | --- | --- |
| 1G-GPON | 4 | SFF(Class B+) | 1:64 | No |
| 1G-GPON | 8 | SFP(Class B+ and Class C+) | 1:128 | No |
| 1G-GPON | 8 | SFP(Class B+ and Class C+) | 1:128 | Yes |
| 1G-GPON | 16 | SFP(Class B+ and Class C+) | 1:128 | Yes |
| 1G-GPON | 8 | SFP(Class B+ and Class C+) | 1:128 | Yes |
| 10G-GPON | 4 | XFP | 1:128 | Yes |

Difference between GPON intermediate B + and C + optical modules

- Both of the B + and C + are supported 1:128 spectroscopic, mainly affecting transmission distance

- The higher splitting ratio is, the greater of the loss, and the shorter of the transmission distance

- You can replace the customer GPBD of B + module into C +, but it should be charged

OLT module:

Transmit power   RX Sensitivity   (Unit: dBm)

Class B+:     1.5~5             -28

Class C+:     3~7              -32

ONU module:

Class B+:     0.5~5             -27

Class C+:     0.5~5             -30

Power board

- MA5680T, MA5683T, MA5600T, MA5603T power only supports DC (If you only AC input, you need to buy an inverter to convert AC-48V into DC.)

- MA5608T divided into two kinds, AC and DC.

Software

- The charges is based on each GPON port, from R (n) to R (n +1)

- Software issues related to compatibility between Huawei OLT and Huawei ONT, with some compatibility version is better, and some relatively poor.